PT8613 Serial communication between MCU and FPGA
June 26th 2007 Thomas Holm Hansen

Physical interface
We have 4 signals between the MCU and FPGA:

Signal	Description	Source
cs	Chip select	MCU
sck	Serial clock	MCU
mosi	Master out slave in	MCU
miso	Master in slave out	FPGA

The MCU is master and the FPGA is slave.

-- Example of transmitting and recieving one byte:
-- ----- -----
-- cs: | |
-- ----------------------------------------------------------------------------
-- --- --- --- --- --- --- --- ---
-- sck: | | | | | | | | | | | | | | | |
-- ------------ --- --- --- --- --- --- --- ---------------
-- ------- ------- ------- ------- ------- ------- ------- -------
-- mosi: X msb X b6 X b5 X b4 X b3 X b2 X b1 X lsb X
-- ------------- ------- ------- ------- ------- ------- ------- ------- ------- ----------
-- ------- ------- ------- ------- ------- ------- ------- -------
-- miso: X msb X b6 X b5 X b4 X b3 X b2 X b1 X lsb X
-- ------------- ------- ------- ------- ------- ------- ------- ------- ------- ----------

The mosi signal is clocked into the FPGA just after the falling edge of sck. The MISO signal from the FPGA changes just after the rising edge of sck.

A 3 byte header is always send first from the MCU, followed by the data to/from the FPGA. The header sets the register adress pointer (RAP). The first byte of data is corresponding to the RAP in the header. If more than one byte is send/recieved the register adress is incremented correspondingly for every byte until the communication is stopped by setting the cs to high.

Communication package
Header	byte 0 communication desitnation 0x00: overall module / 0x01: channel 1 / 0x02: channel 2 / 0x04: channel 3 / 0x08: channel 4 / byte 1 - byte 2 16 bit register adress pointer byte1: msb / byte2: lsb
Data	byte 3 -	data	see register mapping below

Register adress	Channel	Lenght (bytes)	Type	Description	Values
0x0000	1 - 4	1	Write	System	0xA0: 1080i/30 / 0xB0: 1080i/29.97 / *0xA1: 1080i/25 / 0x82: 1080p/30 / 0x92: 1080p/29.97 / 0x83: 1080p/25 / 0x84: 1080p/24 / 0x94: 1080p/23.98 / 0xA2: 1080sF/30 / 0xB2: 1080sF/29.97 / 0xA3: 1080sF/25 / 0xA4: 1080sF/24 / 0xB4: 1080sF/23.98 / 0x86: 720p/60 / 0x96: 720p/59.94 / 0x87: 720p/50 / 0x88: 720p/30 / 0x98: 720p/29.97 / 0x89: 720p/25 / 0x8A: 720p/24 / 0x9A: 720p/23.98 / 0x60: NTSC 525i/29.97 / 0x20: PAL 625i/25
0x0001	1 - 4	1	Write	Pattern	0x00:
0x0002	1 - 4	1	Write	Pattern Option (Modify)
0x0003 - 0x0005	1 - 4	3	Write	Timing
0x0006	1 - 4	1	Write	System Interface	*0x00: YCbCr (4:2:2) 10-bit (single-link) / 0x01: YCbCr (4:2:2) 12-bit (dual-link) / 0x02: YCbCr (4:4:4) 10-bit (dual-link) / 0x03: YCbCr (4:4:4) 12-bit (dual-link) / 0x04: RGB (4:4:4) 10-bit (dual-link) / 0x05: RGB (4:4:4) 12-bit (dual-link)
0x0007 - 0x0008	1 - 4	2	Write	Audio click timing	b11 - b0: / 0x1F4: + 500ms / ... / 0x001: + 1ms / *0x000: 0 / 0xFFF: - 1ms / ... / 0xE0C: - 500ms
0x0009	1 - 4	1	Write	Audio signal	*0x01: Sine / 0x02: Click / else: Silence
0x000A	1 - 4	1	Write	Audio level	(0x04: -24 dBFS) / (0x03: -18 dBFS) / (0x02: -12 dBFS) / (0x01: -6 dBFS) / *0x00: 0 dBFS / 0xFF: -1 dBFS / 0xFE: -2 dBFS / 0xFD: -3 dBFS / ... / 0xC4: -60 dBFS
0x000B - 0x000C	1 - 4	2	Write	Horizontal text position
0x000D - 0x000E	1 - 4	2	Write	Vertical text position
0x000F	1 - 4	1	Write	Text scale	b1 - b0: / *0x00: Smallest / 0x01: / 0x02: / 0x03: Largest
x0010	1 - 4	1	Write	Text and background color	b6: R background / b5: G background / b4: B background / b2: R text / b1: G text / b0: B text / *0x07 (white font on black)
0x0011	1 - 4	1	Write	Width of text bitmap	0 - 255
0x0012	1 - 4	1	Write	Hight of text bitmap	0 - 255
0x0013	1 - 4	1	Write	Text movement	b1 - b0: / 0x0: No move / *0x1: Vertical movement / 0x2: Horizontal movement / 0x3: Ver. + hor. movement
0x0014	1 - 4	1	Write	Text on/off	b0: / 0: off / *1: on
0x0080	1 - 4	1	Read / (Sticky)	Channel status	b3: video frame was reset / b2: MGT was reset / b1: MGT fifo error occured / b0: MGT power down occured
0x0081	0	1	Read / (Sticky)	Clock warning	b7: Wrong period detected when reclocking 1.001sec pulse from 27MHz to 148.4MHz or 148.5MHz domain (1 or more) / b6: Wrong period detected when reclocking 1sec pulse from 27MHz to 148.5MHz domain (1 or more) / b5: Change in frame count 30 syncronization (1 or more) / b4: Wrong period detected in f4m sync periods (1 or more) / b3: Change in frame count 25 syncronization (1 or more) / b2: Wrong period detected in f8g sync periods (1 or more) / b1: 148.4MHz PLL excessive phase difference / b0: 148.5MHz PLL excessive phase difference
0x0082	0	1	Read / (Sticky)	Clock related errors	b7: Wrong period detected when reclocking 1.001sec pulse from 27MHz to 148.4MHz or 148.5MHz domain (several) / b6: Wrong period detected when reclocking 1sec pulse from 27MHz to 148.5MHz domain (several) / b5: Change in frame count 30 syncronization (several) / b4: Wrong period detected in f4m sync periods (several) / b3: Change in frame count 25 syncronization (several) / b2: Wrong period detected in f8g sync periods (several) / b1: 148.4MHz PLL out of phase lock / b0: 148.5MHz PLL out of phase lock
0x0088	0	1	Write	Mask on clock related errors (reg 0x0082) before reporting to changeover	b7 – b0: 0: Ignore respective error, 1: Report respective error
0x0089	0	1	Write	Mask on error from channels	b3: 0: Ignore errors from channel 4, 1: Report errors from channel 4 / b2: 0: Ignore errors from channel 3, 1: Report errors from channel 3 / b1: 0: Ignore errors from channel 2, 1: Report errors from channel 2 / b0: 0: Ignore errors from channel 1, 1: Report errors from channel 1
0x0090	0	1	Read	Frame count 25 (Counts a 2x25 frame sequence based on f8g to make an internal 1sec pulse). Since it is impossible to make a johnson sequence on 25, the counting sequence is 50.	"00000000" : frame 0 / "00000001" : frame 1 / "00000011" : frame 2 / "00000010" : frame 3 / "00000110" : frame 4 / "00000111" : frame 5 / "00000101" : frame 6 / "00000100" : frame 7 / "00001100" : frame 8 / "00001101" : frame 9 / "00001111" : frame 10 / "00001110" : frame 11 / "00001010" : frame 12 / "00001011" : frame 13 / "00001001" : frame 14 / "00001000" : frame 15 / "00011000" : frame 16 / "00011001" : frame 17 / "00011011" : frame 18 / "00011010" : frame 19 / "00011110" : frame 20 / "00011111" : frame 21 / "00011101" : frame 22 / "00011100" : frame 23 / "00010100" : frame 24 / "00110100" : frame 0 / "00111100" : frame 1 / "00111101" : frame 2 / "00111111" : frame 3 / "00111110" : frame 4 / "00111010" : frame 5 / "00111011" : frame 6 / "00111001" : frame 7 / "00111000" : frame 8 / "00101000" : frame 9 / "00101001" : frame 10 / "00101011" : frame 11 / "00101010" : frame 12 / "00101110" : frame 13 / "00101111" : frame 14 / "00101101" : frame 15 / "00101100" : frame 16 / "00100100" : frame 17 / "00100101" : frame 18 / "00100111" : frame 19 / "00100110" : frame 20 / "00100010" : frame 21 / "00100011" : frame 22 / "00100001" : frame 23 / "00100000" : frame 24
0x0091	0	1	Read	Frame count 30 (Counts a 30 frame sequence based on f4m to make an internal 1.001sec pulse)	"00000000" : frame 0 / "00000001" : frame 1 / "00000011" : frame 2 / "00000010" : frame 3 / "00000110" : frame 4 / "00000111" : frame 5 / "00000101" : frame 6 / "00000100" : frame 7 / "00001100" : frame 8 / "00001101" : frame 9 / "00001111" : frame 10 / "00001110" : frame 11 / "00001010" : frame 12 / "00001011" : frame 13 / "00001001" : frame 14 / "00101001" : frame 15 / "00101011" : frame 16 / "00101010" : frame 17 / "00101110" : frame 18 / "00101111" : frame 19 / "00101101" : frame 20 / "00101100" : frame 21 / "00100100" : frame 22 / "00100101" : frame 23 / "00100111" : frame 24 / "00100110" : frame 25 / "00100010" : frame 26 / "00100011" : frame 27 / "00100001" : frame 28 / "00100000" : frame 29
0x0092	0	1	Write	Temporary frame count 25 register	A special Johnson count sequence is used to avoid false readings due to unsyncronized reads. (see mapping of reg 0x0090)
0x0093	0	1	Write	Temporary frame count 30 register	A special Johnson count sequence is used to avoid false readings due to unsyncronized reads. (see mapping of reg 0x0091)
0x0094	0	1	Write	Update frame counters	b1: 1: / Syncronize frame count 30 sequence (Implement the 0x0091 register timing) / b0: 1: / Syncronize frame count 25 sequence (Implement the 0x0090 register timing)
0x1000 - 0x1111	1 - 4	Up to 512	Write	Text bitmap data	One bit per pixle