Project progress

01/02/07-15/02/07 Study the DDR2 ram, MIG007
16/02/07-01/03/07 First versions of VHDL test program of the DDR2 ram, the output shows there are different bits in the output results that go wrong
01/03/07-07/03/07 Simulation of the model, timing simulation. Error corrected in the simulation.
07/03/07-17/03/07 Study flash, VHDL test program for flash, failed to read or write
17/03/07-10/04/07 New version of PCB made(V1.5), new connections between DDR2 and FPGA
11/04/07-30/04/07 Study the flash, different approaches towards interfacing flash. Not working correctly.
01/05/07 First test program using MB inside FPGA on ML401 board. Working correctly
01/05/07-14/05/07 Migrating the design onto PT8614
16/05/07 The flash can be read, written or erased by the MB inside V2pro
23/05/07 Test DDR2 ram on the V1.5 board, the first test program works.
30/05/07 Migrate the design into PPC. Can't add a top level to the design. The flash can't output correct data. The possible problem is the IOBUF used in the top level
14/06/07 Test entire DDR2 ram with internal programmed counter. Bigger capacitor on VDDQ, successful

Project Plan

June 2007
The refinement of the flash test program, including: migrate the design into PPC, adding top level module (1-2 days)

Interfacing PPC with rest of the FPGA, implementing a bus which both flash and DDR2 can access. (1 week, before 09/06)

Test the DDR2 thoroughly. Reading and writing all addresses in an optimal way. (1 week, before 15/06)

Building the interface of DDR2 & RocketIO, so the contents of the DDR2 can be displayed on the screen. (1 week)

Building up the communication between flash and DDR2, so DDR2 reads all the data when the system being powered up (how to test?) (1-2 week before 01/07)

July 2007
Optimizing the flash programming method(by using buffer programming or factory programming.(1 week)

Building the interface between 8051 & FPGA. (1 week)

Modifying MSD-load PC program so that an image can be transmitted to 8051 through USB
(1-2 weeks)

Test of the whole system.

Integrating the design with PT8612