PT 5300
HD-SD Varitime™ Sync Generator
with

PT 8611
Tri-Level HDTV Sync Generator

Supplement to: PT 5230	Reference: Manual no. 9499 491 02811

The manual for the PT 5300 is not ready, but as the generator is based on the PT5230, this manual is used as an interim solution.

The supplement describes the new PT8611 Tri-Level HDTV sync generator
The PT8611 has 4 separately controllable tri-level outputs. For each output any of 21 HD formats can be independently selected. For several HD formats genlocking to the frame rates of SD 525-line and 625-line systems will automatically take place. In this way frame synchronisation is ensured between SD and HD.

Each of the 4 Tri-Level outputs can be individually delayed or advanced with respect to the phase of each other and the mainframe system sync or genlock input.

The timing parameters are divided into frame, line and format system clock cycles resulting in a timing resolution of 6.7 ns for all formats

Note:
Some functions have not yet been implemented in the PT5300 and PT8611, a.o.:
- Remote control commands for the PT8611
- Errors codes for PT8611
- Function of “OUTPUT” button
- Number of preset is reduced to 5
- Status menu not complete
- Diagnose menu not complete
Menu: TRI-LEVEL, HDTV Tri-level Sync Generator
This is the menu for setting the parameters for the tri-level outputs. The number of selection entries in the tri-level generator menu varies with the number of tri-level generators installed.

The tri-level outputs are named TLGn, n being the number of the connector on the back of the instrument.

Setting of the TRI-LEVEL generators:
MENU:TRI-LEVEL, configure  / SUBMNU:<TLG1> TLG2 TLG3 TLG4

- Use the or  buttons to select TLG1
- Then press  to enter the submenu for TLG1

SUBMNU:TRI-LEVEL/TLG1,select  / 2NDMNU:<FORMAT> TIMING

The 2NDMNU allows changes to be made in the parameters for the TLG1 output.

To change format, select FORMAT
2NDMNU:../TLG1/FORMAT, select  / FORMAT:<1280x720/60/9> SAVE ESC

Operation:
- Use the  and  buttons to find the system setting you want.
- When the desired system appears in the display, move the cursor to SAVE and press
- EXECUTE to change the system setting
- If no change is desired, move the cursor to ESC and press 
  Leaving the function takes you back to the TRI-LEVEL/TLG1 submenu.
Tri-level generator format options:
The table below also informs about relation to the standard TV systems 525 lines and 625 lines.

Selectable Formats	Active samples / per line	Active lines per frame	Frame rate	Scan / Method	Fields/Frame sync / to SD format
1920x1080/60/P	1920	1080	60	P	Free running
1920x1080/59.94/P	1920	1080	59.94	P	525
1920x1080/50/P	1920	1080	50	P	625
1920x1080/60/I	1920	1080	30	I	Free running
1920x1080/59.94/I	1920	1080	29.97	I	525
1920x1080/50/I	1920	1080	25	I	625
1920x1080/30/P	1920	1080	30	P	Free running
1920x1080/29.97/P	1920	1080	29.97	P	525
1920x1080/25/P	1920	1080	25	P	625
1920x1080/24/P	1920	1080	24	P	Free running
1920x1080/23.98/P	1920	1080	23.98	P	Free running

1920x1035/60/I	1920	1035	30	I	Free running
1920x1035/59.94/I	1920	1035	29.97	I	525

1280x720/60/P	1280	720	60	P	Free running
1280x720/59.94/P	1280	720	59.94	P	525
1280x720/50/P	1280	720	50	P	625
1280x720/30/P	1280	720	30	P	Free running
1280x720/29.97/P	1280	720	29.97	P	525
1280x720/25/P	1280	720	25	P	625
1280x720/24/P	1280	720	24	P	Free running
1280x720/23.98/P	1280	720	23.98	P	Free running
OFF	The output is disabled.

Note:
When changing the format the timing information is recalled from last setting in the appropriate format.

To change the delay/advance timing for the TLG1 output, select TIMING.
2NDMNU:../TLG1/TIMING, edit delay  / F:<+0> H:+008 T: +00124.3 SAVE ESC

Operation:
- Use the or  buttons to select F, H, or T
  F is a field selection between 0 or 1 for interlaced formats, but is always 0 for progressive scan formats.
- Then use the and buttons to change the setting
  Changes to the timing are instantaneous, i.e. any changes are reflected immediately in the output signal
- When the desired setting appears in the display, move the cursor to SAVE and press
- EXECUTE to change the setting

The timing can be adjusted by coarse or fine adjustment parameters. The coarsest adjustment is field (F) for interlaced formats, the finest is time (T), and line (H) is in between. The T value is in nanoseconds.

- The T value can be changed by using the  and  buttons to adjust the smallest step (approx. 6.7ns) for the adjustment, but a faster method is to press EXECUTE when the cursor is on the T value. This opens an editor in which each of the time digits can be changed using the  and  buttons
- Positions are selected by using the  and  buttons
- To exit the editor press EXECUTE

- When the desired delay setting appears in the display, move the cursor to SAVE and press
- EXECUTE
- If no changes are desired, move the cursor to ESC and press 
  Leaving the function takes you back to the TRI-LEVEL/TLG11 submenu.