PT8640 SNTP-Server module for the PT5300.
Specification .

Functions.
1. The PT8640 is implemented using a Silabs C8051F120 MCU and a Silabs CP2200 Ethernet Controller.

2. The IP stack is based on IPv4. (www.xxx.yyy.zzz)

3. DHCP Client. (Can be disabled and use static IP.)

4. Net-Finder Implementation.
(Locating PT8640's on the network without using IP address.
Configuration of IP address and Password.
Net-Finder functions is accessed from a Windows Client.)

5. Simple boot-loader that will enable firmware upgrades of the PT8640 MCU. (Through RS232 interface.)

6. Implementation of SNTP server Version 4 for IPv4. (RFC2030) (No client mode.)
The SNTP server will not be able to handle more than 10 requests per second.

7. Telnet to RS232 converter to interface the PT5300 Mainboard.

8. RS232 interface to the PT5300 Mainboard. (Locked to 9600 Baud, 1 Stop bit, No Parity. No RTS and CTS.)

9. Changeover interface to the PT5300 Mainboard.

10. I2C Slave. Configuration of Ethernet interface and Telnet Password.

11. Max PCB size 90 x 40 mm to make room for SDI board (PT8603 or PT8632).

12. The PCB is 4 Layer with a V-Cut for mounting holes.

Notes.
The PT8616 SDI Genlock module must be installed for the SNTP Server to work.
The PT8616 must supply 1PPS and RS232 TX from UBLOX receiver.
1PPS and RS232 TX from UBLOX is buffered through the Xilinx FPGA.

Since the MCU on the PT8616 is the only one that can communicate with the UBLOX receiver, the MCU	must be implemented with a pin that can be set low to signal the UBLOX receiver to transmit Leap Second	information. (GPS REQUEST)

The MCU on the PT8616 must supply a signal that indicates if the UBLOX receiver is locked.
(GPS LOCK)

All other functions will work without the PT8616 module.

The PT5300 mainboard software must be updated so the RS232 settings can not be changed and a new	menu with Ethernet settings is implemented.

The PT8640 board can be powered either through connnector XK1 on the PT5300 Mainboard or through the	PT8616.

The RS232 signals on the PT8640 is routed through a MAX4571 analogue switch.
This switch has the following settings.
1. RS232 connector on the rear of the PT5300 → PT8640 MCU.
   Firmware upgrade of the PT8640 MCU.

2. RS232 connector on the rear of the PT5300 → PT5300 Mainboard.
   Normal RS232 Communication with the PT5300 Mainboard. (Not using RTS and CTS signals.)

3. PT8640 MCU → PT5300 Mainboard.
   Telnet communication with the PT5300 Mainboard.

Net-Finder Client.